## TECHNICAL PARAMETRES

| TYPE | FAR-2160 LTE PROTECTED DC PASS | FAR-2160 LTE PROTECTED DC BLOCK |
| --- | --- | --- |
| Pass band | MHz | 470-790 |
| Loss at pass band | dB | 4(1,0 |
| Stop band | MHz | 791-862 |
| Stop band attenuation | dB@MHz | 18@800MHz; 30@900 |
| DC pass from output | V DC / mA max. | 5-24 / 100 | - |
| OTHER |  |  |  |
| Impedance input/output | Ohm | 75 / 75 |
| Connectors type | / | fmale „F” / male „F” |
| Operating temperature range | (C | -20…+50 |

## EXAMPLE OF APPLICATION

# Text boxes

# Band stop filter LTE

# FAR-2160 LTE PROTECTED/

# FAR-2160 LTE PROTECTED DC PASS

RoHS

FAR-2160 is the band stop filter. It is dedicated 
for cut noise from frequency range: 790-862MHz (LTE). Filter transmits signals 470-790MHz (K21-60).

FPL-2160 is a indoor device with SAW technology which is able to sharply cut LTE signals, and transmits 
DVB-T signals.

There are two versions: with DC pass and without DC PASS.